## Slide 1: Multiplexing and de-multiplexing
Chapter-4

## Slide 2: introduction
Multiplexing (or muxing) is a way of sending multiple signals or streams of information over a communications link at the same time in the form of a single, complex signal;
The receiver recovers the separate signals, a process called DE multiplexing (or demuxing).
Multiplexing and demultiplexing are performed by a Multiplexer (also called a MUX) which usually has both capabilities.

## Slide 4
MUX
Multiplexer
Multiplexing
Analog
Digital
De-Multiplexing
FDM
WDM
TDM
CDM
Synchronous
TDM
Asynchronous
TDM

## Slide 5: What is a Multiplexing ?
Multiplexing is a technique that enable broadband media to support multiple data channels.
  Multiplexing can enable :
    Mainframe , LAN , Voice, Video conferencing , other data type.
  Large amounts of data must be transmitted through low capacity channels.
  Multiplexing techniques can divide the original data stream into several lower-bandwidth channels, each of which can be transmitted though a lower-capacity medium.

## Slide 7: Analog & Digital signal
analog is a continuous electrical signal, whereas digital is a non-continuous electrical signal.
Analog waves are smooth and continuous, digital waves are stepping, square, and discrete.

## Slide 8: Types of multiplexing
FDM
WDM
TDM
CDM

## Slide 9
MUX
Multiplexing
Analog
Digital
De-Multiplexing
FDM
WDM
TDM
CDM
Synchronous
TDM
Asynchronous
TDM

## Slide 10: FDM (Frequency division multiplexing)
Frequency Division Multiplexing (FDM) is a networking technique in which multiple data signals are combined for simultaneous transmission via a shared.
Frequency Division Multiplexing (FDM) is a scheme in which numerous signals are combined for transmission on a single communications line or channel.
FDM uses a carrier signal at a discrete frequency for each data stream and then combines many modulated signals.

## Slide 11: TDM (Time division multiplexing)
Time-division multiplexing (TDM) is a method of putting multiple data streams in a single signal by separating.
the signal into many segments, each having a very short duration. Each individual data stream is reassembled at the receiving end based on the timing.

## Slide 12: WDM (Wavelength division multiplexing)
Wavelength-division multiplexing (WDM) is a method of combining multiple signals on laser beams at various infrared (IR) wavelengths for transmission along fiber optic media. Each laser is modulated by an independent set of signals.

## Slide 13: (CDM)Code division multiplexing
Code Division Multiplexing assigns each channel its own code to make them separate from each other. These unique underlying codes.
Code division multiplexing (CDM) is a networking technique in which multiple data signals are combined for simultaneous transmission over a common frequency band.